## Slide 1
ROBOTICS

## Slide 2: PROJECT 1
LED Traffic Light System

## Slide 3: What is a Traffic Light System?
A traffic light system is a set of coloured lights that control vehicle and pedestrian movement at intersections.

## Slide 4
It typically consists of three coloured lights:
Red: Indicates that vehicles must stop. Pedestrians may be allowed to cross, depending on the intersection rules.
Yellow (or Amber): Warns that the light is about to change to red. Drivers should prepare to stop if it is safe to do so.
Green: Indicates that vehicles may proceed. Pedestrians typically must wait for the signal to cross.

## Slide 5: Materials Required
Arduino Uno
Breadboard
Resistors(3-220Ω, Pull-Up 10kΩ)
LEDs (Red, Yellow, Green)
Buzzer
Push button
Jumper wire (male-to-male)

## Slide 6: Materials Required
Arduino Uno: Is a microcontroller board that acts as the brain of the project, processing inputs and controlling outputs.
Breadboard: Is a reusable platform for building circuits without soldering, allowing easy connections and modifications.
Resistor: It limit the flow of current in a circuit; the pull-up resistor keeps a pin at a high state when no button is pressed.
LEDs: Are Light-emitting diodes that indicate status or signals; each color can represent a different state (e.g., on/off).

## Slide 7: Materials Required
Buzzer: Is a sound-producing device that generates beeps or tones based on electrical signals from the Arduino.
Push Button: Is a switch that allows users to send a digital signal to the Arduino when pressed, typically used for user input.
Jumper Wire: Are flexible wires used to make connections between components on the breadboard or to the Arduino.

## Slide 8
Arduino uno
Breadboard

## Slide 9
Jumper wires (male-to-male)
LEDs
Resistors

## Slide 10
Jumper wires (male-to-female)
USB cable
Buzzer
Push button

## Slide 11: Real life application of traffic light system
Intersections
Pedestrian Crossings
Emergency Vehicle Priority
Public Transport Management
Smart Traffic Management
School Zones

## Slide 12: Circuit connection
LED Connection
Insert the three LEDs into the breadboard
Insert 3 - 220Ω resistors into the anode column of each LED
Connect the other end of the resistors to pins 11,12,13, that is, RED=>11, YELLOW=>12, GREEN=>13.
Connect the LEDs cathodes to the negative terminal.
Connect the negative terminal to the ground,GND.

## Slide 13
LEDs connection

## Slide 14: Circuit connection(Cont’d)
Buzzer connection
Insert the buzzer into the breadboard.
Connect the positive terminal (+) to pin 8.
Connect the negative terminal (-) of the buzzer to the negative terminal of the breadboard.

## Slide 15
LEDs connection with buzzer

## Slide 16: Circuit connection(Cont’d)
Push button connection
Insert the push button into the breadboard.
Connect a terminal to pin 7
Connect a terminal to negative terminal of the breadboard or the ground, GND.
Connect a 10kΩ resistor to another terminal of the push button.
Connect the other end of the resistor to 5v pin in the Arduino uno.

## Slide 17
LEDs connection with buzzer and push button

## Slide 18: THANK YOU
See you in the next class!!!